## Slide 1: Fundamentals of Computer Science and Programming
Unit 3 – Boolean Algebra and Numeral Systems

## Slide 2: Outline
Boolean Algebra
Numeral systems
Conversion between numeral systems
Binary arithmetic

## Slide 3: Boolean Algebra

## Slide 4: Boolean Algebra
Boolean algebra is related to propositional logic
It provides the operations and the rules for working with the set
The three operations from the Boolean algebra that we will use:
  Complement denoted with
  Boolean sum (OR) denoted with
  Boolean product (AND) denoted with ⋅ (can be omitted)
Connection to propositional logic is straightforward
  Set corresponds to
  Complement: , (Negation)
  Sum:
    (Logical or)
  Product:
    (Logical and)

## Slide 5: Boolean algebra
Example 1: Find the value of .

## Slide 6: Boolean variables and functions
Variable is called a Boolean variable if it takes values from
A function , from to is called a Boolean function of degree
Values of Boolean functions are often displayed in tables (similar to truth tables)
Representation of a Boolean function with the value when and otherwise.
1 | 1 | 0
1 | 0 | 1
0 | 1 | 0
0 | 0 | 0
1 | 1 | 0
1 | 0 | 1
0 | 1 | 0
0 | 0 | 0

## Slide 7: Boolean expressions and functions
Boolean functions can be represented using expressions
Boolean expressions are made from variables and Boolean operations
We then introduce further expressions recursively as follows:
  are Boolean expressions
  If and are Boolean expressions
    , are also Boolean expressions

## Slide 8: Boolean algebra
Example 2: Find the values of the Boolean function represented by
.
1 | 1 | 1 | 1 | 0 | 1
1 | 1 | 0 | 1 | 1 | 1
1 | 0 | 1 | 0 | 0 | 0
1 | 0 | 0 | 0 | 1 | 1
0 | 1 | 1 | 0 | 0 | 0
0 | 1 | 0 | 0 | 1 | 1
0 | 0 | 1 | 0 | 0 | 0
0 | 0 | 0 | 0 | 1 | 1
1 | 1 | 1 | 1 | 0 | 1
1 | 1 | 0 | 1 | 1 | 1
1 | 0 | 1 | 0 | 0 | 0
1 | 0 | 0 | 0 | 1 | 1
0 | 1 | 1 | 0 | 0 | 0
0 | 1 | 0 | 0 | 1 | 1
0 | 0 | 1 | 0 | 0 | 0
0 | 0 | 0 | 0 | 1 | 1

## Slide 9: Boolean identities
Boolean identities. | 
Identity | Name
 | Identity Laws
 | Domination Laws
 | Idempotent Laws
 | Double Complement Law
Boolean identities. | 
Identity | Name
 | Identity Laws
 | Domination Laws
 | Idempotent Laws
 | Double Complement Law
Logical equivalences from propositional logic translate to Boolean algebra
They are called Boolean identities

## Slide 10: Boolean identities
Boolean identities. | 
Identity | Name
 | Commutative Laws
 | Associative Laws
 | Distributive Laws
 | De Morgan‘s Laws
Boolean identities. | 
Identity | Name
 | Commutative Laws
 | Associative Laws
 | Distributive Laws
 | De Morgan‘s Laws

## Slide 11: Boolean algebra
Example 3: Using Boolean identities show that:
De Morgan
Distributive Law
Distributive Law
Contradiction

## Slide 12: Exercise

## Slide 13: Student task
Task 1: The Boolean operator ⊕, called the XOR operator (logical exclusive or), is defined by 1 ⊕ 1 = 0, 1 ⊕ 0 = 1, 0 ⊕ 1 = 1, and 0 ⊕ 0 = 0. Simplify the following expressions.
Show that the following identity holds:
.
Recollect that:
,
and hence:
.

## Slide 14: Numeral systems

## Slide 15: Numeral systems
Decimal system
Binary system
Octal system
Hexadecimal system
Arbitrary system
https://www.i-programmer.info/images/stories/BabBag/hex/hand16.png
https://commons.wikimedia.org/wiki/File:Led_light_bulb_-_led_lamp_2.png
https://en.wikipedia.org/wiki/File:Hand_INC.svg
http://pngimg.com/download/29445
?

## Slide 16: Decimal system
Base 10, digits: 0 to 9
Position system
  Every position (index) has a single digit b
  Value at a given index i :
  Resulting number: sum of all position values

## Slide 17: Decimal system
Example 4: Numbers in decimal system.
Number | 1313 | 842
Index i | 3 2 1 0 | 2 1 0
Digit | 1 3 1 3 | 8 4 2
Values |  | 
Result | 1000 300 10 3 | 800 40 2
Number | 1313 | 842
Index i | 3 2 1 0 | 2 1 0
 | 1 3 1 3 | 8 4 2
Values |  | 
Result | 1000 300 10 3 | 800 40 2
Number | 12345
Index i | 4 3 2 1 0
Digit | 1 2 3 4 5
Values | 
Result | 10000 2000 300 40 5
Number | 12345
Index i | 4 3 2 1 0
 | 1 2 3 4 5
Values | 
Result | 10000 2000 300 40 5

## Slide 18: Binary system
Base 2, digits: 0 and 1
  False and True, switch off and on
Position system
  Every position (index) has a single digit b
  Value at a given index i :
  Resulting number: sum of all position values

## Slide 19: Binary system
Example 5: Numbers in binary system.
Binary | 11 | 1101
Index i | 1 0 | 3 2 1 0
Digit | 1 1 | 1 1 0 1
Values |  | 
Result | 2 1 | 8 4 0 1
Decimal | 3 | 13
Binary | 11 | 1101
Index i | 1 0 | 3 2 1 0
 | 1 1 | 1 1 0 1
Values |  | 
Result | 2 1 | 8 4 0 1
Decimal | 3 | 13
Binary | 11110010
Index i | 7 6 5 4 3 2 1 0
Digit | 1 1 1 1 0 0 1 0
Values | 
Result | 128 64 32 16 0 0 2 0
Decimal | 242
Binary | 11110010
Index i | 7 6 5 4 3 2 1 0
 | 1 1 1 1 0 0 1 0
Values | 
Result | 128 64 32 16 0 0 2 0
Decimal | 242

## Slide 20: Counting in powers of two
Important concept: counting in powers of two
Collection of 8 positions (0 - 7): 1 Byte
Index i | 9 8 7 6 5 4 3 2 1 0
Power of 2 | 
Values | 
Example | 1 1 0 1 0 1 1 1 0 1
Result | = 861
Index i | 9 8 7 6 5 4 3 2 1 0
Power of 2 | 
Values | 
Example | 1 1 0 1 0 1 1 1 0 1
Result | = 861

## Slide 21: Counting in powers of two
Source: slideplayer.com

## Slide 22: Octal system
Base 8, digits: 0 to 7
Position system
  Every position (index) has a single digit b
  Value at a given index i :
  Resulting number: sum of all position values

## Slide 23: Octal system
Example 6: Numbers in octal system.
Octal | 16 | 7650
Index i | 1 0 | 3 2 1 0
Digit | 1 6 | 7 6 5 0
Values |  | 
Result | 8 6 | 3584 384 40 0
Decimal | 14 | 4008
Octal | 16 | 7650
Index i | 1 0 | 3 2 1 0
 | 1 6 | 7 6 5 0
Values |  | 
Result | 8 6 | 3584 384 40 0
Decimal | 14 | 4008
Octal | 1230321
Index i | 6 5 4 3 2 1 0
Digit | 1 2 3 0 3 2 1
Values | 
Result | 262144 65536 12288 0 192 16 1
Decimal | 340177
Octal | 1230321
Index i | 6 5 4 3 2 1 0
 | 1 2 3 0 3 2 1
Values | 
Result | 262144 65536 12288 0 192 16 1
Decimal | 340177

## Slide 24: Octal system
Octal system is a readable representation of the binary system
Hence, we can group three digits from a binary number into a single octal digit
Binary | 11 | 1101 | 11110010
Groups | 11 | 1 101 | 11 110 010
Value | 3 | 1 5 | 3 6 2
Octal | 3 | 15 | 362
Decimal | 3 | 13 | 242
Binary | 100010100010100010
Groups | 100 010 100 010 100 010
Value | 4 2 4 2 4 2
Octal | 424242
Decimal | 141474

## Slide 25: Hexadecimal system
Basis 16, digits: 0 to 9 and 10 – 15 but we use letters A – F
A means 10, B means 11, C means 12, D means 13, E means 14, F means 15
Position system
  Every position (index) has a single digit b
  Value at a given index i :
  Resulting number: sum of all position values

## Slide 26: Hexadecimal system
Example 7: Numbers in hexadecimal system.
Hexadecimal | 11 | CAFE
Index i | 1 0 | 3 2 1 0
Digit | 1 1 | C A F E
Values |  | 
Result | 16 1 | 49152 2560 240 14
Decimal | 17 | 51966
Hexadecimal | 11 | CAFE
Index i | 1 0 | 3 2 1 0
 | 1 1 | C A F E
Values |  | 
Result | 16 1 | 49152 2560 240 14
Decimal | 17 | 51966
Hexadecimal | C0FFEE
Index i | 5 4 3 2 1 0
Digit | C 0 F F E E
Values | 
Result | 12582912 0 61440 3840 224 14
Decimal | 12648430
Hexadecimal | C0FFEE
Index i | 5 4 3 2 1 0
 | C 0 F F E E
Values | 
Result | 12582912 0 61440 3840 224 14
Decimal | 12648430

## Slide 27: Hexadecimal system
Hexadecimal system is a readable representation of the binary system
We can group four digits from a binary number into a single hexadecimal digit
  Hence, with two hexadecimal digits we can represent one byte
Binary | 1101 | 11110010 | 100010100010100010
Groups | 1101 | 1111 0010 | 10 0010 1000 1010 0010
Value | D | F 2 | 2 2 8 A 2
Hexa | D | F2 | 228A2
Decimal | 13 | 242 | 141474

## Slide 28: Numbers table
Binary | Octal | Decimal | Hexadecimal
0 | 0 | 0 | 0
1 | 1 | 1 | 1
10 | 2 | 2 | 2
11 | 3 | 3 | 3
100 | 4 | 4 | 4
101 | 5 | 5 | 5
110 | 6 | 6 | 6
111 | 7 | 7 | 7
1000 | 10 | 8 | 8
1001 | 11 | 9 | 9
1010 | 12 | 10 | A
1011 | 13 | 11 | B
1100 | 14 | 12 | C
1101 | 15 | 13 | D
1110 | 16 | 14 | E
1111 | 17 | 15 | F

## Slide 29: Numbers table
Binary | Octal | Decimal | Hexadecimal
10000 | 20 | 16 | 10
10001 | 21 | 17 | 11
10010 | 22 | 18 | 12
10011 | 23 | 19 | 13
10100 | 24 | 20 | 14
10101 | 25 | 21 | 15
10110 | 26 | 22 | 16
10111 | 27 | 23 | 17
11000 | 30 | 24 | 18
11001 | 31 | 25 | 19
11010 | 32 | 26 | 1A
11011 | 33 | 27 | 1B
11100 | 34 | 28 | 1C
11101 | 35 | 29 | 1D
11110 | 36 | 30 | 1E
11111 | 37 | 31 | 1F

## Slide 30: Conversion between numeral systems

## Slide 31: Numeral systems conversions
Position systems:
: highest index, starting with 0
: index
: Base ≥ 2
: digit at index
Convert to decimal: use above formula, see examples from previous slides
Binary to other systems
  Grouping, see examples from previous slides
Convert between arbitrary systems, e.g., decimal to other systems:
  Division and remainder algorithm

## Slide 32: Division and remainder
Decimal number to any other numeral system with the base :
with remainder
Set , store
If repeat from step 1
Else output all remainders in the opposite order of storing them

## Slide 33: Division and remainder
Example 8: Convert (131)10 to binary.
131 / 2 = 65 Remainder = 1
65 / 2 = 32 Remainder = 1
32 / 2 = 16 Remainder = 0
16 / 2 = 8 Remainder = 0
8 / 2 = 4 Remainder = 0
4 / 2 = 2 Remainder = 0
2 / 2 = 1 Remainder = 0
1 / 2 = 0 Remainder = 1
(131)10 = (10000011)2

## Slide 34: Division and remainder
Example 9: Convert (142)10 to hexadecimal.
142 / 16 = 8 Remainder = 14 (E)
8 / 16 = 0 Remainder = 8
(142)10 = (8E)16

## Slide 35: Exercise

## Slide 36: Student task
Task 2: Convert the numbers between numeral systems.
(245)10 to binary, octal, and hexadecimal system.
(14D)16 to binary, octal, and decimal system.
(231)8 to binary, decimal, and hexadecimal system.
(1001100)2 to octal, decimal, and hexadecimal system.

## Slide 37: Binary arithmetic

## Slide 38: Arithmetic operations with binary numbers
Basic arithmetic operations
  Addition
  Negative numbers
  Subtraction
Multiplication and division can be implemented by repeated addition/subtraction
Least significant bit (LSB)
  Rightmost (last) position
Most significant bit (MSB)
  Leftmost (first) position
Index i | n … 7 6 5 4 3 2 1 0
Power of 2 | 
Values | 
Index i | n … 7 6 5 4 3 2 1 0
Power of 2 | 
Values | 

## Slide 39: Addition of binary numbers
Basic operation | 
+ | First number
 | Second number
c | Carry
= | Result
0 + 0 = 0 |  | 
+ | 0 | 0
 | 0 | 0
c | 0 | 0
= | 0 | 0
1 + 0 = 1 |  | 
+ | 0 | 1
 | 0 | 0
c | 0 | 0
= | 0 | 1
0 + 1 = 1 |  | 
+ | 0 | 0
 | 0 | 1
c | 0 | 0
= | 0 | 1
1 + 1 = (0, c) = 10 |  | 
+ | 0 | 1
 | 0 | 1
c | 1 | 0
= | 1 | 0
1+1+1=(1, c)=11 |  | 
+ | 0 | 1
 | 0 | 1
c | 1 | 1
= | 1 | 1

## Slide 40: Addition of binary numbers
45 + 54 = 99 |  |  |  |  |  |  |  |  | 
 | 64 | 32 | 16 | 8 | 4 | 2 | 1 |  | Position value
+ | 0 | 1 | 0 | 1 | 1 | 0 | 1 |  | First number = 45
 | 0 | 1 | 1 | 0 | 1 | 1 | 0 |  | Second number = 54
c | 1 | 1 | 1 | 1 | 0 | 0 | 0 |  | Carry
= | 1 | 1 | 0 | 0 | 0 | 1 | 1 |  | Result = 99
341 + 444 = 785 |  |  |  |  |  |  |  |  |  |  |  | 
 | 512 | 256 | 128 | 64 | 32 | 16 | 8 | 4 | 2 | 1 |  | Position value
+ | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 |  | First number = 341
 | 0 | 1 | 1 | 0 | 1 | 1 | 1 | 1 | 0 | 0 |  | Second number = 444
c | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 0 | 0 |  | Carry
= | 1 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 1 |  | Result = 785

## Slide 41: Exercise

## Slide 42: Student task
Task 3: Add the numbers in binary numeral system.
25 and 67
34 and 12
112 and 123
200 and 33
x + y = ? |  |  |  |  |  |  |  |  |  | 
 | 128 | 64 | 32 | 16 | 8 | 4 | 2 | 1 |  | Position value
+ |  |  |  |  |  |  |  |  |  | First number
 |  |  |  |  |  |  |  |  |  | Second number
c |  |  |  |  |  |  |  |  |  | Carry
= |  |  |  |  |  |  |  |  |  | Result = ?

## Slide 43: Negative numbers
Representation we used so far
  Unsigned number range, which is always positive or 0
To represent negative numbers we convert numbers to their complement
There are several complement conversion methods
We will learn Two’s Complement:
  Complement all bits (One‘s Complement)
  Add 1 (Two‘s Complement)
We will reserve MSB for the sign of the number:
  MSB is 1 for negative numbers and 0 for positive numbers

## Slide 44: Negative numbers
Example 10: Find two‘s complement of 45 represented with one byte.
0 | 0 | 1 | 0 | 1 | 1 | 0 | 1 |  | = 45
1 | 1 | 0 | 1 | 0 | 0 | 1 | 0 |  | Ones‘ complement of 45
0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 |  | +1
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |  | Carry
1 | 1 | 0 | 1 | 0 | 0 | 1 | 1 |  | Result = -45

## Slide 45: Negative numbers
Example 11: Adding a number with its two‘s complement results in zero.
45 + (-45) = 0 |  |  |  |  |  |  |  |  |  |  | 
+ |  | 0 | 0 | 1 | 0 | 1 | 1 | 0 | 1 |  | = 45
 |  | 1 | 1 | 0 | 1 | 0 | 0 | 1 | 1 |  | = -45
c | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0 |  | Carry
= | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |  | Result = 0
Complement is used to complete the number range
Positive number + its two‘s complement (negative number) = 0

## Slide 46: Ones’ and two’s complement
Why does it work?
Ninth bit is carry-out bit and is discarded in an 8-bit representation. The result, 00000000 = 0, is correct: no overflow
Signed representation has the number range:
  1 byte = 8 bits: [-128, 127]
Example 12: Theory behind ones‘ and two‘s complement.
 | 0 | 0 | 1 | 0 | 1 | 1 | 0 | 1 |  | = 45
 | 1 | 1 | 0 | 1 | 0 | 0 | 1 | 0 |  | Ones‘ comp.
 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 |  | 
 | 1 | 1 | 0 | 1 | 0 | 0 | 1 | 1 |  | Two’s comp. + 1
1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |  | 
 | 0 | 0 | 1 | 0 | 1 | 1 | 0 | 1 |  | 
 | 1 | 1 | 0 | 1 | 0 | 0 | 1 | 0 |  | 
 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 |  | 
 | 1 | 1 | 0 | 1 | 0 | 0 | 1 | 1 |  | 
1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |  | 

## Slide 47: Signed binary representation
https://texample.net/media/tikz/examples/PNG/complement.png
0 | 1 | 1 | 0 |  | = 6
1 | 0 | 0 | 1 |  | Ones‘ comp. of 6
0 | 0 | 0 | 1 |  | +1
0 | 0 | 1 | 0 |  | Carry
1 | 0 | 1 | 0 |  | Result = -6
6 + (-6) = 0 |  |  |  |  |  |  | 
+ |  | 0 | 1 | 1 | 0 |  | = 6
 |  | 1 | 0 | 1 | 0 |  | = -6
c | 1 | 1 | 1 | 0 | 0 |  | Carry
= | 1 | 0 | 0 | 0 | 0 |  | Result = 0

## Slide 48: Negatives of negative numbers
Example 13: Find two‘s complement of -45 represented with one byte.
1 | 1 | 0 | 1 | 0 | 0 | 1 | 1 |  | = -45
0 | 0 | 1 | 0 | 1 | 1 | 0 | 0 |  | Ones‘ complement of -45
0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 |  | +1
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |  | Carry
0 | 0 | 1 | 0 | 1 | 1 | 0 | 1 |  | Result = 45
Two‘s complement works also for negative numbers
  Negative of a negative number gives us the positive number

## Slide 49: Unsigned vs signed representation
How can one binary number represent two decimal numbers?
  Computers interpret them differently
Unsigned: without sign, only positive numbers
  All bits used for number representation
  Number range:
  Examples: (10010000)2 = (144)10 , (11010011)2 = (211)10
Signed: with sign, positive and negative numbers
  MSB keeps the sign: 1 is negative, 0 is positive
  Number range:
  Examples: (10010000)2 = (-112)10, (11010011)2 = (-45)10

## Slide 50: Importance of number ranges
-29 + (-13) = -42 |  |  |  |  |  |  |  |  |  |  | 
+ |  | 1 | 1 | 1 | 0 | 0 | 0 | 1 | 1 |  | = -29
 |  | 1 | 1 | 1 | 1 | 0 | 0 | 1 | 1 |  | = -13
c | 1 | 1 | 1 | 0 | 0 | 0 | 1 | 1 | 0 |  | Carry
= | 1 | 1 | 1 | 0 | 1 | 0 | 1 | 1 | 0 |  | Result = -42
-68 + (-101) = -169 |  |  |  |  |  |  |  |  |  |  | 
+ |  | 1 | 0 | 1 | 1 | 1 | 1 | 0 | 0 |  | = -68
 |  | 1 | 0 | 0 | 1 | 1 | 0 | 1 | 1 |  | = -101
c | 1 | 0 | 1 | 1 | 1 | 0 | 0 | 0 | 0 |  | Carry
= | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 1 | 1 |  | Result = 87
Wrong result because we are outside of the range: [-128, 127] Carry-out discarded as before, but the result is wrong: overflow

## Slide 51: Subtraction of binary numbers
Subtraction is addition with a negative number
Hence, represent , as signed binary numbers
Compute two‘s complement of
Add and
Technically, addition is fast
  We need only machinery for addition

## Slide 52: Exercise

## Slide 53: Student task
Task 4: Find the two‘s complements of these numbers using one byte.
25
67
200
133
 |  |  |  |  |  |  |  |  | = x
 |  |  |  |  |  |  |  |  | Ones‘ complement of x
 |  |  |  |  |  |  |  |  | +1
 |  |  |  |  |  |  |  |  | Carry
 |  |  |  |  |  |  |  |  | Result = ?

## Slide 54: Student task
Task 5: Subtract these numbers using one signed byte.
25 and 12
67 and 33
110 and 101
 |  |  |  |  |  |  |  |  | = x
 |  |  |  |  |  |  |  |  | Ones‘ complement of x
 |  |  |  |  |  |  |  |  | +1
 |  |  |  |  |  |  |  |  | Carry
 |  |  |  |  |  |  |  |  | Result = ?
x + (-y) = ? |  |  |  |  |  |  |  |  |  | 
 | Sign | 64 | 32 | 16 | 8 | 4 | 2 | 1 |  | Position value
+ |  |  |  |  |  |  |  |  |  | First number
 |  |  |  |  |  |  |  |  |  | Second number
c |  |  |  |  |  |  |  |  |  | Carry
= |  |  |  |  |  |  |  |  |  | Result = ?

## Slide 55: Multiplication and division of binary numbers
Multiplication is typically carried out by repeated addition
  There are more efficient algorithms for multiplication
  These include shifting bits to the left
Division is typically carried out by repeated subtraction
  More efficient algorithms exist